## Slide 1
HTR: On-Chip Hardware Task Relocation for Partially Reconfigurable FPGAs
+ Also Affiliated with NSF Center for High-Performance Reconfigurable Computing
Aurelio Morales-Villanueva and Ann Gordon-Ross+
Department of Electrical and Computer Engineering
University of Florida, Gainesville, Florida, USA
This work was supported by National Science Foundation (NSF) grants EEC-0642422 and IIP-1161022, and Programa de Ciencia y Tecnología (FINCyT) under contract 121-2009-FINCyT-BDE

## Slide 2: Introduction
Multitasking in modern systems
  Software tasks: implemented in microprocessors
  Hardware tasks: implemented in field-programmable gate arrays (FPGAs)
Task management requirements in any multitasking system
  Task scheduling
    Mechanism to begin task execution on a system resource
  Task suspension
    Preempt task and saving execution state --- context save (CS)
  Task switching
    Replacing preempted task with another task
  Task restoration
    Resume preempted task from saved state --- context restore (CR)
T7
T’4
T3
T’2
T1
time
A
B
Task
T’6
T5
T’4
T3
T’2
T1
time
A
B
C
Task
Task
T6
T5
T4
T3
T2
T1
time
A
B
C

## Slide 3: Context Switching Analogy
Multiple tasks execute concurrently
Multiple regions time multiplex tasks
  Use context save and context restore for task switching
Task relocation
  Challenging!
Leveraging partial reconfiguration can be advantageous…
One task executes at a time
  Time multiplex tasks
One stack for all tasks
  Stack saves context for task restore
No task relocation
No reconfiguration of uP
Hardware task N
Hardware task 2
Hardware task 1
uP or
custom HW
Region 3
Region 2
Region 1
FPGA
FPGA Context Switch
Software task N
Software task 2
Software task 1
Stack
OS
+
MMU
uP
Processor Context Switch

## Slide 4: Reconfiguration on FPGAs
Benefits to system designers and functionality
  Run-time hardware adaptation via time multiplexing of resources
  Reduced area/power requirements
  Two types of reconfiguration: Full and partial reconfiguration
Full reconfiguration:
  Entire FPGA configured with full bitstream with fixed hardware task set
  Reconfiguration halts all tasks --- lengthy task switching time
  No context save/restore ofhardware tasks --- tasks restart execution
Execution and state of all tasks is lost during full reconfiguration!
Configuration Port
Full bitstream 2
Full bitstream 1
HW task C1
HW task B1
HW task A1
HW task C2
HW task B2
HW task A2
Unless state can be saved via checkpoint of data capture

## Slide 5: Partial Reconfiguration (PR)
  Increased flexibility
  Increased task throughput/performance
  Enhances hardware multitasking
    Requires context save and context restore for effective task switching
PR compared to full reconfiguration
  Dynamic, on-the-fly PR of individual PRRs
    No interruption of static region or other PRRs!
  Uses partial bitstreams --- smaller than full bitstreams
    Faster reconfiguration time
    *May* require a bitstream for each PRM-to-PRR mapping
PR divides the FPGA fabric into two regions
  Static region: fixed functionality, never reconfigured after initial configuration at startup
  Reconfigurable region: multiple PR regions (PRRs)
    PRRs execute PR modules (PRMs) (hardware tasks)
Function
Power On
Time
Static region operation
Reconfiguration
Overhead
Configuration
Overhead
Module D
Module C
Module B
Module A
Embedded
processor
ICAP
Mem Controller
Reconfig. region
Static region

## Slide 6: Previous Related Work
Context save and restore (CSR)
  Over the same PRR using:
    Off-chip CSR software
      Requires external host (e.g., CPU)
      Lengthy communication overhead
    On-chip CSR hardware
      Device overhead, limited portability
  No task re-execution after context restore
Bitstream relocation (BR)
  Eliminates per-PRR bitstream requirement
  Off/on-chip BR over homogeneous PRRs
    Same shape/resources, different FPGA fabric locations
  Does not save/restore task’s context
    Re-execution of relocated task required
  No relocation over heterogeneous PRRs
PRMs
custom
relocate +
reconfigure
reconfigure
reconfigure
PRMs
homogeneous
PRRs
custom
HW
context restore
task’s context
task’s context
context save
context save
reconfigure
reconfigure

## Slide 7: Motivations
Improvements over off-chip context save and restore (CSR) software
  Eliminate external host requirement --- autonomous
  Eliminate communication overhead between FPGA and external host
Improvements over on-chip context save and restore (CSR) hardware
  Eliminate custom hardware requirement and area overhead
  Eliminate portability limitations
Improvements over bitstream relocation (BR)
  Enable task relocation over heterogeneous PRRs
  Eliminate task re-execution requirement

## Slide 8: Contributions
On-chip hardware task relocation (HTR) software
  Relocation of hardware tasks over heterogeneous PRRs
    PRRs with different shape, resources, locations on the FPGA fabric
  Relocation of hardware task context
    Task’s execution state is preserved --- no re-execution
HTR benefits
  Maximizes shared resources utilization
    Reduces idle PRRs --- PRMs can run in any available PRR*
  Maximizes task throughput
    Improves task scheduling performance
    Preemption and resumption of tasks in different PRRs
      Priority considerations
    Eliminates lengthy re-execution time of relocated preempted tasks
* Some restrictions apply, but are addressed in our current/future work

## Slide 9: Hardware Task Relocation (HTR)

## Slide 10: HTR Operation
Still Busy
Context
Save
Context
Save
Context
Restore
M2
PRR4
M3
PRR3
M6
PRR4
M5
PRR3
M4
PRR2
M5
PRR2
M1
PRR1
Task
Relocation
M2
PRR1
Still Busy
Resume
Operation
Use initial
partial bitstream
Resume
Operation
Use initial
partial bitstream
Task
Relocation
Context
Restore
Main HTR software steps
  Initialize static region and PRRs
    Initial configuration of tasks in all PRRs
  Context save (CS)
    Save the execution state of the preempted hardware task
  Task relocation (TR)
    Generation of a “merged bitstream” of relocated task
  Context restore (CR)
    Resume execution of preempted task in another PRR

## Slide 11: HTR Flow Chart
Example system
Execute PRM2 on PRR2
Context restore of PRM2 on PRR2
TCR2
Saved context relocation of PRM2 in PRR2
Trelocate
Context save of PRM3
TCS2
Hardware task relocation (HTR) of PRM2 on PRR2
Execute PRM2 on PRR1
Context restore of
PRM2 on PRR1
TCR1
Merge saved context of PRM2 with initial bitstream of PRM2
Tmerge
Context save of PRM1
TCS1
Context save and restore (CSR)
N
Y
PRR1 free or priority PRM
Execute PRM2
N
Y
Reconfiguration of PRR1 with PRM1
Enable FPGA protection
Tprotect_FPGA
Treconfig_PRR
Initialization
PRR2
PRR1
PRM3
Merged PRM2
PRM2
PRM
2
PRM
1
PRM2 executed in PRR1
and saved the context
Executing PMR3
Initial conditions

## Slide 12: Experimental Results

## Slide 13: Experimental Setup
Virtex-5 LX110T on Xilinx ML509 board
Two reconfigurable regions (PRRs)
  Contain configurable logic block (CLB) resources (flip-flops)
  Heterogeneous sizes and FPGA fabric locations
Task relocation cases
  Small-to-large PRR task relocation
  Large-to-small PRR task relocation
  Source PRR = PRR with task’s saved context
  Destination PRR = PRR with task’s relocated context
  Restrict test cases for tractability
    Large PRR = 2x (number of columns and frames of small PRR)
    Number of flip-flops used by the task are the same for all PRR sizes
Notes: For the purpose of HTR, two PRRs have different locations in the FPGA fabric.
There are two cases for relocation: from small-to-large PRR or from large-to-small PRR
The third case is not interesting: same-size PRR relocation
Since there are so many combination (I think 144 for consecutive CLB columns) to perform a task relocation (in terms of sizes between two PRRs), I reduced the experiments (went down to 12) by having the large PRR with double (2x) the number of columns of the small PRR.
Since we covered only CLBs, doubling the number of columns in the large PRR, also doubles the number of frames.

## Slide 14: Results – Context Save (TCS)
Context save time shows linear growth rate
Dependent on the number of PRM frames in the source PRR
(per column)
Notes: Number of FFs per column

## Slide 15: Results – Task Relocation (Trelocate)
Task relocation time shows non-linear growth rate
  Random access pattern to saved context and merged bitstreams
  High data cache misses and overheads accessing data from SDRAM
Dependent on the number of PRM flip-flops to be relocated

## Slide 16: Results – Context Restore (TCR)
Context restore time shows nearly linear growth rate
Dependent on the number PRR frames in the merged bitstream (destination PRR)
Context restore time is larger than PRR reconfiguration time (Treconfig_PRR)
  Unprotection and protection of destination PRR

## Slide 17: Conclusions
Introduced on-chip hardware task relocation (HTR) software
  Task relocation between heterogeneous PRRs
    Maximizes shared resource utilization
  No off-chip communication overhead
  No design/system constraints
  Application/system independent
  Aids system design
    Enables designers to tradeoff HTR execution times and task/PRR granularity
Future work
  Extend HTR’s functionalities
    Include DSP, BRAM, and IOB resources in PRRs

## Slide 18: Questions?